## Slide 1: Introduciton to mobile Robotics
Project – 2026
Tatiana, Laura Gómez, Daniel Gebauer
Notes: Overview - Create® 3 Docs for the picutre

## Slide 2: Table of Contents
Project Definition
Architecture
Implementaiton
Results

## Slide 3: Project Defintion
goals and Requirements

## Slide 4: Desired Behaviour
Initial Boot & Undocking
Autonomous Exploration
Proportional Obstacle Avoidance:
  AWARE zone: slowdown. WARNING zone: braking CLOSE zone: stop and turn
Hazard Recovery:
  Recover from bumper contact with obstacle
Timed Return-to-Dock
Human Override:
  TELEOP for manual control

## Slide 5: Architecture
Design Decisions

## Slide 7: Design Decisions
2 Node achitecture:
  Manual control
  Exploration and obstactle avoidance
Communication via topics
  Subsciber and publisher
  Organisation of communication
  Callback methods on message receive

## Slide 8: Design Decisions
Global State of the Explorer
  Easy conditional Behaviour
  Extendable framework for additional features

## Slide 9: Implementation

## Slide 10: Obstacle Avoidance
Subscribe to ir-sensor topic
On message arrival, execute obstacle check:
  7 different sensors
  Check returns against threshold
  Determine direction from sensor position
On detection initiate avoidance

## Slide 11: Manual Control
keyboard logger running constantly
On interrupt:
  sent message to change status of the explorer node
In manual mode:
  Read commands from keystrokes
  Relay commands to robot
Return to automatic:
  Change mode of explorer node

## Slide 12: Return to Dock
Final docking handled by docking server
  Only works in proximity to Station
Navigate back to Dock
  Explore Until Dock is detected
  Keep obstacle avoidance active on way to dock
  Seperate state to keep tack of docking goal
Manual mode for accelerated docking

## Slide 13: LED Status
Indicate Status of the Robot

## Slide 14: Results
Demonstration

## Slide 15: Anyone got a video?

## Slide 16: Sources
The pictures are taken form the create3 website: Create® 3 Docs